## Slide 1
dGen: Distributed Wind Model Assumptions
Presentation to DOE Wind Program
Ian-Baring Gould, Ben Sigrin, Robert Preus, and Mike Gleason
November 15, 2015

## Slide 2: Presentation Objective
Describe proposed default settings for major dGen model assumptions
Identify and discuss areas for improvement and gain DOE guidance on plans for resolution

## Slide 3: Presentation Overview
Review key model dynamics
Review core framework for modeling diffusion of technology
Summary of major assumptions
  Wind-specific and tech agnostic
Detailed review of each major assumption
  Default settings
  Basis for settings
  Known areas for improvement
  Planned future work (Q1-Q2)

## Slide 4: Key Model Dynamics
Models the deployment of distributed wind for behind-the-meter customers only
  Includes: individual households and businesses making independent investment choice for an on-site wind system
  Excludes: community wind, wind gardens, utility wind, virtual net-metering
Relationship to REEDS [Ben – please revise this as necessary]
  REEDS models capacity expansion of utility (wholesale) wind generation
  dGen models market growth in single-customer distributed wind generation
  No overlap between the two
  Neither accounts for community wind or wind gardens
System sizes:
  Turbine sizes range from 2.5 kw to 1.5 mw
  For heavy industrial users, multiple 1.5 mw turbines may be installed
Competition between technologies:
  The solar and wind markets are generally modeled in isolation, which assumes no competition
  We recently added a feature to facilitate modeling of competition, but have not tested it thoroughly
[Ben, Ian, Eric] What other points do we need to clarify for DOE?
Notes: This is a good point to stop and ensure that DOE has no other questions about basic model dynamics.

## Slide 5: Core Model Framework: Modeling Diffusion
[ all ] should we add a brief slide here outlining the basics of how economic attractiveness is translated to diffusion via max market share curves and the Bass diffusion process?
If so, Ben should prepare this

## Slide 6: Summary of Model Assumptions (Wind-Specific)
Assumption | Level of Support | Basis of Support
Turbine Performance (Current) | High | Empirical + Engineering Judgment + Analysis
Turbine Performance (Future) | High | Engineering Judgment?
Turbine Performance Improvement Schedule | Low | Empirical + Analysis
Installation Costs (Current) | Medium | Empirical + Engineering Judgment
Installation Costs (Future) | Low | Empirical + Analysis
O&M Costs (Current) | Medium | Engineering Judgment?
O&M Costs (Future) | Low | Empirical + Engineering Judgment
Financing | High | Empirical
Incentives | Low | Empirical + Analysis
[All] Do we want to include future projections in this presentation given the state they are currently in?
Notes: Note:
Empirical = based on data
Empirical + Analysis = based on NREL analysis of empirical data
Engineering Judgment = based on logical decisions made by NREL on the basis of domain expertise and/or research

## Slide 7: Summary of Model Assumptions (Tech Agnostic)
Assumption | Level of Support | Basis of Support
Electricity Rates and Rate Escalations | High | Empirical + Analysis
Net Metering | High | Empirical
Maximum Market Share Curves | High | Empirical
Load Growth | High | Empirical
Notes: Note:
Empirical = based on data
Empirical + Analysis = based on NREL analysis of empirical data
Engineering Judgment = based on logical decisions made by NREL on the basis of domain expertise and/or research

## Slide 8
Detailed Model Assumptions: Wind-Specific

## Slide 9: Turbine Performance (Current)
Overview:
  8 power curves in dGen
  4 representing current turbines
Basis of Support:
  Empirical: Reviewed [Robert: insert number] power curves for various size existing turbines
  Analysis: Normalized power curves by rated power, constructed generic representative power curves with equal swept area and normalized annual energy
Planned Future Work:
  Review by TRC
Power Curve | Rotor Efficiency (m2/kWp) | Capacity Factor | Power Curve ID
Current Small Residential (2.5‑20 kw) | 3.07 | 0.29 | 1
Current Small Commercial (50‑100 kw) | 4.9 | 0.375 | 2
Current Midsize (250‑1000 kw) | 3.1 | 0.42 | 3
Current Large (1500 kw) | 4.9 | 0.385 | 4
Default Settings:
[Mike/Ben] Add a back up slide all 8 actual power curves on them?

## Slide 10: Turbine Performance (Future)
Overview:
  Remaining 4 power curves represent near future and far future turbines
Basis of Support:
  Engineering Judgment: Considered the maturity of existing tech at different size classes and the technical factors limiting tech improvements
Planned Future Work:
  Review by TRC
Power Curve | Rotor Efficiency (m2/kWp) | Capacity Factor | Power Curve ID
Near Future Small Residential (2.5‑20 kw) | 4.0 | 0.385 | 5
Far Future Small Residential (2.5‑20 kw) | 5.2 | 0.40 | 6
Near Future Small Commercial to Large (50-1500 kw) | 4.2 | 0.43 | 7
Large (1500 kw) | 5.2 | 0.44 | 8
Default Settings:
[Robert] Be prepared to succinctly explain the specific assumptions and judgments you made for these

## Slide 11: Turbine Performance (All)
[Mike/Ben] Consider adding the graphic with all power curves here. Use better color coding and line styles to thematically group by size class and type period.

## Slide 12: Turbine Performance Improvement Schedule
Overview:
  Power curves are assigned to each turbine size for each model year
Default Settings:
Turbine Size (kw) | 2014 | 2016 | 2018 | 2020 | 2022 | 2024 | 2026 | 2028 | 2030 | 2032 | 2034 | 2036 | 2038 | 2040 | 2042 | 2044 | 2046 | 2048 | 2050
2.5 | 1 | 1 | 5 | 5 | 5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
5 | 1 | 1 | 5 | 5 | 5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
10 | 1 | 1 | 5 | 5 | 5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
20 | 1 | 1 | 5 | 5 | 5 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
50 | 2 | 2 | 2 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
100 | 2 | 2 | 2 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
250 | 3 | 3 | 7 | 7 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
500 | 3 | 3 | 7 | 7 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
750 | 3 | 3 | 7 | 7 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
1000 | 3 | 3 | 3 | 7 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
1500 | 4 | 4 | 4 | 4 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8
ID | Power Curve
1 | Current Small Residential-Scale Turbine
2 | Current Small Commercial-Scale Turbine
3 | Current Mid-Size Turbine
4 | Current Large Turbine
5 | Near Future Small Residential-Scale Turbine
6 | Far Future Small Residential-Scale Turbine
7 | Small, Mid-Size, and Large Near Future Turbine
8 | Small, Mid-Size, and Large Far Future Turbine
Basis of Support:
  [in progress]
Planned Future Work:
  [in progress]
[Ben/Mike] Update schedule with final version from Robert
[Robert] are there important transition points we want to call out here?

## Slide 13: Installation Costs (Current)
Overview:
  Two parameters for costs:
    Baseline capital costs ($/kw) based on default tower height
    Marginal costs for taller towers above default height
Basis of Support:
  Empirical: Reviewed project cost information from [Robert: add count] datasets; interviewed [Robert: add count] manufacturers
  Analysis: Determined median costs for systems at various heights and for marginal tower height costs
Areas for Improvement:
  Sparse data available for marginal tower costs for 250-750 kw turbines
Default Settings:
Turbine Rated Power (kW) | Baseline Capital Cost ($/kW) | Full Cost ($) | Default Turbine Height (m) | Marginal Tower Cost ($/kW*m)
2.5 | $10,045 | $25,113 | 20 | $211
5 | $7,785 | $38,925 | 30 | $164
10 | $6,914 | $69,145 | 30 | $118
20 | $6,459 | $129,186 | 30 | $71
50 | $5,858 | $292,879 | 30 | $15.70
100 | $5,402 | $540,238 | 40 | $11.30
250 | $3,525 | $881,232 | 50 | $10.80
500 | $2,961 | $1,480,283 | 50 | $9.90
750 | $2,630 | $1,972,827 | 50 | $9.00
1,000 | $2,396 | $2,396,206 | 80 | $8.10
1,500 | $2,185 | $3,277,628 | 80 | $6.40
Planned Future Work:
  Additional research into tower costs for 250-750 kw turbines

## Slide 14: Installation Costs (Future)
Overview:
  Costs for each turbine size are specified for each model year
Basis of Support:
  [in progress]
Areas for Improvement:
  [in progress]
Default Settings:
  [Add graphic show cost trajectories, once they are determined]
Planned Future Work:
  Review by TRC

## Slide 15: O&M Costs (Current)
Overview:
  Fixed O&M costs account for scheduled and unscheduled maintenance
  Assume no variable O&M [be prepared to justify this]
Basis of Support:
  Empirical: Interviewed [Robert: add count] manufacturers, leasing companies, installers, and consultants
  Analysis: Fit linear regression to collected data to estimate O&M costs at model turbine sizes
Areas for Improvement:
  Lacking data for unscheduled maintenance at size extremes (2.5-10 kw and 750-1500 kw)
  Insufficient sample size to capture important mechanical transitions around 50-100 kw
Default Settings:
Planned Future Work:
  Additional data collection/interviews focused on extreme size classes
  If sufficient data available, fit separate regressions for 2.5-50 kw and 50-1500 kw
Turbine Rating (kW) | Scheduled O&M ($/kW) | Unscheduled O&M ($/kW) | Total Fixed O&M ($/kW)
2.5 | 27.64 | 11.3 | $38.94
5 | 27.62 | 11.3 | $38.92
10 | 27.58 | 11.3 | 38.88
20 | 27.5 | 11.3 | 38.8
50 | 27.27 | 11.29 | 38.56
100 | 26.87 | 11.28 | 38.15
250 | 25.69 | 11.25 | 36.94
500 | 23.71 | 11.2 | 34.91
750 | 21.74 | 11.15 | $32.89
1000 | 19.76 | 11.1 | $30.86
1500 | 15.81 | 11 | $26.81

## Slide 16: O&M Costs (Future)
Overview:
  O&M costs for each turbine size are specified for each model year
Basis of Support:
  [in progress]
Areas for Improvement:
  [in progress]
Default Settings:
  [Add graphic show O&M cost trajectories, once they are determined]
Planned Future Work:
  Review by TRC

## Slide 17: Financing (Current)
Overview:
  Financing parameter specified separately for each business model and market sector
Basis of Support:
  Empirical: [Ben: add notes on data sources for various financing parameters]
Areas for Improvement:
  Lessor hurdle rates are based on historical rates for solar leasing companies
Default Settings:
[Ben: add charts with default settings]
Planned Future Work:
  Contact wind leasing companies (United Wind) to request information on leasing parameters

## Slide 18: Financing (Future)
Overview:
  Financial parameters can also be specified to vary by model year
Basis of Support:
  [in progress]
Planned Future Work
  Review by financial modeling experts within NREL’s Strategic Energy Analysis Center
Default Settings:
[Ben: add charts with default settings]

## Slide 19: Incentives (Federal)
Overview:
  Federal ITC level can be specified by market sector and model year
Basis of Support:
  Engineering Judgement: Assume continuation of existing ITC policy under business-as-usual
Planned Future Work
  Review by TRC
Default Settings:
Year | Residential | Commercial | Industrial
2014 | 30% | 30% | 30%
2016 | 30% | 30% | 30%
2018 | 0% | 10% | 10%
2020 | 0% | 10% | 10%
2022 | 0% | 10% | 10%
2024 | 0% | 10% | 10%
2026 | 0% | 10% | 10%
2028 | 0% | 10% | 10%
2030 | 0% | 10% | 10%
2032 | 0% | 10% | 10%
2034 | 0% | 10% | 10%
2036 | 0% | 10% | 10%
2038 | 0% | 10% | 10%
2040 | 0% | 10% | 10%
2042 | 0% | 10% | 10%
2044 | 0% | 10% | 10%
2046 | 0% | 10% | 10%
2048 | 0% | 10% | 10%
2050 | 0% | 10% | 10%

## Slide 20: Incentives (State and Local)
Overview:
  State and local incentives can either be sourced from DSIRE database or user-defined inputs
Basis of Support/Default Setting:
  Empirical: DSIRE database is used as the default source for state and local incentives
Areas of Improvement:
  DSIRE data has not been updated since 2013 and is missing key information (e.g., expiration dates)
Planned Future Work
  Replace/update DSIRE data with policy data from PNNL

## Slide 21
Detailed Model Assumptions: Technology-Agnostic

## Slide 22: Electricity Rates (Current)
Overview:
  Three options for rates:
    Real-world tariffs based on the Utility Rate Database (URDB)
    Annual average flat rates by county (EIA 861)
    User-defined flat rates by state
Basis of Support/Default Setting:
  Empirical: Real-world tariffs from the URDB are the default setting. These most closely resemble the current electricity costs incurred by electricity consumers in the US.
Planned Future Work
  Review by TRC

## Slide 23: Electricity Rate Escalations (Future)
Overview:
  Options include four rate escalation scenarios based on AEO, or no change
Basis of Support:
  Empirical: AEO 2014 & 2015 Reference Case projections provide rate escalations through 2040
  Analysis: We extended these scenarios through 2075 using two methods – Constant rate of growth from 2040-2075, and time-series projection from 2040-2075
  Engineering Judgment: We use AEO 2015 (Constant after 2040) as the default because it is the most recent and conservative option
Planned Future Work
  Review by TRC
Default Settings:
AEO 2015 (Constant after 2040)
[Ben or Mike: add graphic showing five rate escalation options (nationally) with AEO 205 constant highlighted]

## Slide 24: Net Energy Metering Policies (Current and Future)
Overview:
  Net Energy Metering (NEM) outflow credit valuation and maximum system size can be set by state and sector
  NEM expiration years can also be set by state
Basis of Support/Default Setting:
  Empirical: Default NEM maximum system sizes by state and sector are derived from Barnes et al. (2013).
  Empirical: Non-NEM outflow credit valuation is based on projected wholesale electricity rates by state and model year from [ben: add ref]
  Analysis: Default NEM expiration years by state are based comparison of a recent dGen BAU run for the solar market against cumulative state NEM limits from Barnes et al. (2013).
Planned Future Work
  If necessary and feasible, default NEM expiration years will be updated to account for both the solar and wind markets, using the most recent BAU model assumptions for both technologies

## Slide 25: Maximum Market Share Curves
Overview:
  Maximum market share (MMS) curves relate economic attractiveness to long-term market potential
  The model includes several sources for MMS curves
Basis of Support:
  Empirical: The model includes several published MMS curves for host-owned systems, and one curve for leased systems
  Engineering Judgment: We use curves from Paidipati et al. (2008) for host-owned systems for consistency with previous research (SunShot Vision Study) and because it is less extreme than other options. We use the only available curve for leased systems
Areas for Improvement:
  The default MMS curves are all based on the solar market [do we need to add some text here for further justification?]
Default Settings:
Host-Owned MMS: Paidipati et al. (2008)
[Ben or Mike: add graphic showing MMS curve from navigant]
Leased MMS: Sigrin and Drury (2013)
[Ben or Mike: add graphic showing MMS curve from willingness to pay research]
[all] could trim this down if we decide include slide at the beginning outlining how diffusion works
Planned Future Work:
  May update leasing MMS curve using more recent solar data
  Review by TRC

## Slide 26: Load Growth Projections (Future)
Overview:
  Load growth is implemented in the model as population growth in each sector
  10 load growth scenarios are available, all from AEO 2014 and 2015
Basis of Support:
  Empirical: AEO 2014 & 2015 Reference Case projections provide 5 different scenarios each.
  Engineering Judgment: We use AEO 2015 (Reference Case) as the default because it is the most up-to-date, business-as-usual case available from AEO
Planned Future Work
  Review by TRC
Default Settings:
AEO 2015 (Reference Case)
[Ben or Mike: add graphic showing different load growth scenarios?]

## Slide 27: Summary
[ all ] should we bother including a conclusions/summary slide?

## Slide 28
Additional Information

## Slide 29: Include back up slides, if needed
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet

## Slide 30
Sample Section Divider

## Slide 31: Sample Text Slide with Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet

## Slide 32: Sample 2-Column Slide with Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet
Column 1 Title
Column 2 Title

## Slide 33: Sample Text and Object Slide with Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet

## Slide 34: Sample Text and Object Slide with Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet

## Slide 35: Sample Text Slide without Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet

## Slide 36: Sample 2-Column Slide without Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet
Column 1 Title
Column 2 Title

## Slide 37: Sample Text and Object Slide without Bar
Sample main point
  Sample sub-bullet
    Sample sub-bullet
      Sample sub-bullet